## Slide 1
IIOT SECURITY
IIoT security
from sensor integrity
to incident response
Two complementary architectures protect the control path and the network path.
Notes: Frame the presentation around two complementary security views: the integrity of the control path and the visibility of the network path.

## Slide 2
DESIGN RATIONALE
Why the design uses two architectures
Each architecture answers a different security question. Shared evidence connects the answers.
Architecture 1
Detects tampered sensor readings and protects control commands.
Architecture 2
Detects suspicious network behavior and supports server-side investigation.
Shared evidence
Shared timestamps, device IDs, evidence, and incident records connect the two views.
Notes: Explain that the split is deliberate. One architecture protects message meaning and control decisions; the other observes behavior across the network and server.

## Slide 3
ARCHITECTURE 1 · VERIFIED CONTROL PATH
Sensor integrity before control action
Read, authenticate, classify, then execute only verified commands.
1 · INPUT Water-quality sensors · pH · Turbidity · Electrical conductivity
2 · ACQUIRE ESP32 #1 sensor acquisition · Read sensor values · Add device ID, timestamp + sequence number · Generate HMAC-SHA-256
3 · COMMUNICATION LINK 1 Wi-Fi · HTTPS/MQTT over TLS · authenticity · replay protection
4 · CLASSIFY Laptop — IIoT security server
Message verification · verify HMAC and freshness
Feature extraction · sensor values, trends and historical deviations
Random Forest ML · classify readings
NORMAL · follow control policy
SUSPICIOUS · alert and log evidence
COMMUNICATION LINK 2 authenticated commands · replay protection · expiry checks
ESP32 #2 — PLC-like controller · Verify commands · Enforce local safety limits · Execute control logic
5 · ACTUATORS · LED · buzzer · simulated pump / diversion valve
CONTROL PRINCIPLE · verify the sender, prove freshness, classify the signal, then enforce safety locally.
Notes: Walk the editable architecture from left to right. Water-quality sensors provide pH, turbidity, and electrical conductivity values to ESP32 #1, which adds device identity, timestamp, sequence number, and an HMAC-SHA-256 signature. Communication Link 1 carries only authenticated, replay-protected telemetry to the laptop-based IIoT security server. The server verifies HMAC and freshness, extracts sensor trends and historical deviations, and uses Random Forest ML to classify readings as normal or suspicious. Normal readings follow control policy; suspicious readings trigger an alert and evidence log. Communication Link 2 carries authenticated commands with replay protection and expiry checks to ESP32 #2, which verifies commands, enforces local safety limits, and executes control logic for the LED, buzzer, simulated pump, or diversion valve.

## Slide 4
ARCHITECTURE 1 · PROTECTION LAYERS
What the first architecture protects
01
Identity & integrity
ESP32 #1 adds device identity, timestamps, sequence numbers, and HMAC-SHA-256 integrity protection.
02
Authenticated transport
Wi-Fi and HTTPS/MQTT over TLS add authenticated transport and replay protection.
03
Server verification
The server verifies HMAC and freshness, extracts trends and deviations, then classifies readings with Random Forest.
04
Constrained response
Suspicious readings trigger alerts and evidence logging; verified commands continue through local safety limits.
Notes: Emphasize the order: establish identity and message integrity, secure transport, verify and classify on the server, then constrain the response with alerts, evidence, and local safety limits.

## Slide 5
ARCHITECTURE 2 · NETWORK PATH
Network threat detection and server security
Observe IIoT traffic, detect anomalous behavior, and preserve evidence for investigation.
1. IIoT network traffic · ESP32 #1 ↔ laptop / server ↔ ESP32 #2
2. TShark / Wireshark capture · capture observable network packets
3. Live packet ingestion + flow aggregation
Extract flow features: protocol, ports, packet count, byte count, duration, traffic rates
4. ML network detection
Random Forest · classifies known attack types from labeled traffic
Isolation Forest · flags unusual or novel network behavior
5. Threat detection and alerting · normal / suspicious / malicious traffic
6. Evidence store + incident investigation
Flow records · predictions · timestamps · logs · PCAP references · incident timeline
7. Streamlit security dashboard · live alerts · suspicious connections · attack summaries · incident history
Notes: Network traffic moves from ESP32 #1 through the laptop or server to ESP32 #2. TShark/Wireshark captures packets; live ingestion aggregates flows; Random Forest and Isolation Forest detect known and novel threats; alerts, evidence, and the incident timeline feed the Streamlit investigation view.

## Slide 6
ARCHITECTURE 2 · DETECTION PIPELINE
What the second architecture detects
01
Capture
Capture packets without changing the communication path.
02
Aggregate flows
Aggregate flows and extract IPs, ports, protocols, packet counts, byte counts, duration, and traffic rates.
03
Detect
Use Random Forest for known attack types and Isolation Forest for unusual network behavior.
04
Preserve
Store predictions, timestamps, logs, PCAP references, and incident timelines for investigation.
Notes: Separate the observation mechanism from the analytical roles. Packets are captured passively, flows provide structured fields, the two models cover known and unusual behavior, and the evidence remains available for investigation.

## Slide 7
CORRELATION LOGIC
How the architectures work together
01
Verify sensor messages and control commands.
02
Monitor the same endpoints and server for suspicious traffic.
03
Correlate sensor findings, network events, and control responses by time and device identity.
04
Present one incident history for triage and reconstruction.
Notes: Read the four steps as one investigation path. Message verification and network monitoring become more useful when they share time and device identity, allowing the incident history to support both triage and reconstruction.

## Slide 8
INVESTIGATION VIEW
One dashboard, one investigation view
Streamlit brings live readings, alerts, device status, suspicious connections, attack timelines, and incident history together.
Streamlit
dashboard
One investigation view
SQLite-backed services preserve readings, verification results, predictions, and incident records.
OUTCOME
Defense in depth: verify, detect, constrain, record, and investigate.
Notes: Close on the operational view. The dashboard unifies live readings, alerts, device and connection status, timelines, and history, while SQLite-backed services preserve the evidence behind the investigation.